## Slide 1: HNDIT2401 Computer Architecture
Week 2: Boolean Algebra & Circuit Simplification

## Slide 2: Boolean Algebra
Formal logic: In formal logic, a statement (proposition) is a declarative sentence that is either true(1) or false (0). It is easier to communicate with computers using formal
Boolean variable: They are variables. Takes only two values – either true (1) or false (0). They are used as basic units of formal logic.
Boolean algebra: Deals with binary variables and logic operations operating on those variables.

## Slide 3: Boolean Algebra………
Boolean Expressions: Combining the variables and operators yields Boolean expressions.
Boolean function: Mapping from Boolean variables to a Boolean value. A Boolean function typically has one or more input values and yields a result, based on these input values, in the range {0,1}
Truth table:
  Represents relationship between a Boolean function and its binary variables.
  It enumerates all possible combinations of arguments and the corresponding function values.

## Slide 4: Boolean Algebra………….
• Logic diagram: Composed of graphic symbols for logic gates. A simple circuit sketch that represents inputs and outputs of Boolean functions.

## Slide 5: Boolean function and truth table

## Slide 6: BASIC IDENTITIES OF BOOLEAN ALGEBRA
Postulate 1 (Definition): A Boolean algebra is a closed algebraic system containing a set K of two or more elements and the two operators · and + which refer to logical AND and logical OR
Notes: Postulate -Hypothesize

## Slide 7: Basic Identities of Boolean Algebra (Identity law/dominance (Null) law)
  Identity law
x + 0 = x
x · 1 = x
  dominance (Null) law
x · 0 = 0
x + 1 = 1

## Slide 8: Basic Identities of Boolean Algebra (Idempotent Law / complement law)
  Idempotent Law
(5) x + x = x
(6) x · x = x
  complement law
(7) x + = 1 / x+x’=1
(8) x · = 0 / x.x’=0

## Slide 9: Basic Identities of Boolean Algebra (Commutative law):
(9) x + y = y + x
(10) xy = yx

## Slide 10: Basic Identities of Boolean Algebra (Associative law):
(11) x + ( y + z ) = ( x + y ) + z
(12) x (yz) = (xy) z

## Slide 11: Basic Identities of Boolean Algebra (Distributive law):
(13) x ( y + z ) = xy + xz
(14) x + yz = ( x + y )( x + z)

## Slide 12: Basic Identities of Boolean Algebra (DeMorgan’s Theorem)
(15) = / (x+y)’=x’y’
(16) = /(xy)’=x’+y’

## Slide 13: Basic Identities of Boolean Algebra (Double Complement Law/Involution)
(17) = x/ (x’)’=x

## Slide 14: Basic Identities of Boolean Algebra

## Slide 15: Function Minimization using Boolean Algebra
Examples:
(a) a + ab = a(1+b)=a
(b) a(a + b) = a.a +ab=a+ab=a(1+b)=a.
(c) a + a'b = (a + a')(a + b)=1(a + b) =a+b
(d) a(a' + b) = a. a' +ab=0+ab=ab

## Slide 16: Try
F = abc + abc’ + a’c
Notes: abc + abc’ + a’c
=ab(c+c’)+a’c
=ab(1)+a’c
=ab+a’c

## Slide 17: The other type of question
Show that;
1- ab + ab' = a
2- (a + b)(a + b') = a
1- ab + ab' = a(b+b') = a.1=a
2- (a + b)(a + b') = a.a +a.b' +a.b+b.b'
= a + a.b' +a.b + 0
= a + a.(b' +b) + 0
= a + a.1 + 0
= a + a = a

## Slide 18: More Examples
Show that;
(a) ab + ab'c = ab + ac
(b) (a + b)(a + b' + c) = a + bc
  (a) ab + ab'c = a(b + b'c)
  = a((b+b').(b+c))=a(b+c)=ab+ac
(b) (a + b)(a + b' + c)
= (a.a + a.b' + a.c + ab +b.b' +bc)
= …

## Slide 19: DeMorgan's Theorem
(a) (a + b)' = a'b'
(b) (ab)' = a' + b'
Generalized DeMorgan's Theorem
(a) (a + b + … z)' = a'b' … z'
(b) (a.b … z)' = a' + b' + … z‘

## Slide 20: DeMorgan's Theorem
F = ab + c’d’
F’ = ??
F = ab + c’d’ + b’d
F’ = ??

## Slide 21: DeMorgan's Theorem
Show that: (a + b.c)' = a'.b' + a'.c'
Notes: (a + b.c)' =a’.(bc’)’=a’.(b’+(c’)’)=a’b’+a’.c

## Slide 22: More DeMorgan's example
Show that: (a(b + z(x + a')))' =a' + b' (z' + x')
  (a(b + z(x + a')))' = a' + (b + z(x + a'))'
  = a' + b' (z(x + a'))'
  = a' + b' (z' + (x + a')')
  = a' + b' (z' + x'(a')')
  = a' + b' (z' + x'a)
  =a‘+b' z' + b'x'a
  =(a‘+ b'x'a) + b' z'
  =(a‘+ b'x‘)(a +a‘) + b' z'
  = a‘+ b'x‘+ b' z‘
  = a' + b' (z' + x')

## Slide 23: More Examples
(a(b + c) + a'b)'=b'(a' + c')
ab + a'c + bc = ab + a'c
(a + b)(a' + c)(b + c) = (a + b)(a' + c)

## Slide 24: Karnaugh maps
Circuit Minimization
  Algebraic manipulations can be used to simplify Boolean expressions
    As we've seen, this process is not always easy
  Karnaugh maps (K-maps) provide an easy and visual technique for finding the minimum cost Sum Of Product (SOP) (or Product of sum(POS)) form for a Boolean expression
    This technique has limitations. i.e. works for # inputs < 7
    Not good for CAD tools, but good for teaching the idea of simplification

## Slide 25: Rule for k map
Groups may not include any cell containing a zero
Groups may be horizontal or vertical, but not diagonal.
Rule for k map…………….

## Slide 27
The Combining Property
  Recall the combining property
    x y + x y' = x (y + y') = x
  Example:
    f = x1'x2'x3'+x1'x2x3'+x1x2'x3'+x1x2'x3 = m0 + m2 + m4 + m5
    A minterm is a Boolean expression resulting in 1 for the output of a single cell, and 0s for all other cells in a Karnaugh map, or truth table.
    Minterms m0 and m2 differ in only one variable (x2)
      m0 and m2 can be combined to get x1'x3'
      Reduced fan in and reduced number of gates
    Hence, f = x1'x3' + x1x2'  still SOP but not canonical

## Slide 28
Visualizing the Combining Property
  f(x1,x2) = m(0,1,3)
  Canonical SOP:
    f = x1'x2'+x1'x2+x1x2 = x1'x2'+x1'x2+x1x2+x1'x2 = x1'+x2
  A 2-variable Karnaugh map:
x1 | x2 | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x2 x1 | 0 | 1
0 | 1 | 1
1 | 0 | 1
minimum form: f = x1'+x2

## Slide 29
3 Variable Map
  f(A,B,C) = m(1,2,6,7)
    Minimum SOP is f = A B + B C' + A' B' C
    Cost = gates + fan-in = 4 + (7+3) = 14
B C A | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1
Gray Code: any two consecutive numbers differ in only a single bit

## Slide 30
K-maps in Various Sizes
B C A | 00 | 01 | 11 | 10
0 | m0 | m1 | m3 | m2
1 | m4 | m5 | m7 | m6
B A | 0 | 1
0 | m0 | m1
1 | m2 | m3
C D A B | 00 | 01 | 11 | 10
00 | m0 | m1 | m3 | m2
01 | m4 | m5 | m7 | m6
11 | m12 | m13 | m15 | m14
10 | m8 | m9 | m11 | m10

## Slide 31
Full-Adder Carry-Out
  Cout(A,B,Cin) = m(3,5,6,7)
    Minimum SOP is Cout = A Cin + B Cin + A B
    Cost = 4 + 9 = 13
B Cin A | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1

## Slide 32
More 3 Variable Maps
B C A | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
B C A | 00 | 01 | 11 | 10
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1
A' B + A B' (A  B)
A' + B
f =
f =

## Slide 33
And Even More 3 Variable Maps
B C A | 00 | 01 | 11 | 10
0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
B C A | 00 | 01 | 11 | 10
0 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
A' C + A C' (A  C)
C' + A B
f =
f =

## Slide 34
Full-Adder Sum
  S(A,B,Cin) = m(1,2,4,7)
    Minimum is S = A B' Cin' + A' B' Cin + A B Cin + A'B Cin'
    Can't reduce anything and stay in SOP form!
B Cin A | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0

## Slide 35
Sidebar: Gray Codes
  A binary Gray code is a binary sequence such that no two consecutive numbers differ by more that a single bit
  Gray codes have many uses in CS
    2 bit Gray code: 00, 01, 11, 10
    Note that this is circular  10, 00 again differs in only 1 bit
    These are called binary reflected Gray codes
    3 bit Gray code: 000, 001, 011, 010, 110, 111, 101, 100

## Slide 36
The Formal Karnaugh Map Method
  Choose a 1 element
  Find all maximal groups of 1's adjacent to that element
      Note: "box" must be a power of 2 in size
  Repeat steps 1-2 for all 1 elements
  Select all boxes for which a 1 is “covered” by only that box
      These boxes are essential!
  For all 1's not covered by the essential boxes, select the smallest number of other boxes that cover them
      In case of a choice, select the largest box!

## Slide 37
4 Variable Maps
  f(A,B,C,D) = m(0,1,2,3,6,8,9,11,13,14)
  f = A C' D + B C D' + B' C ' + B' D + A'B'
C D A B | 00 | 01 | 11 | 10
00 | 1 | 1 | 1 | 1
01 | 0 | 0 | 0 | 1
11 | 0 | 1 | 0 | 1
10 | 1 | 1 | 1 | 0

## Slide 38
Another 4 Variable Map
  f(A,B,C,D) = m(0,1,2,5,6,7,8,9,10,13,15)
  f = B D + A' B C + B' D' + B' C' or
  f = B D + A' B C + B' D' + C' D (there are 2 more)
C D A B | 00 | 01 | 11 | 10
00 | 1 | 1 | 0 | 1
01 | 0 | 1 | 1 | 1
11 | 0 | 1 | 1 | 0
10 | 1 | 1 | 0 | 1
These are not essential!

## Slide 39
Terminology
  An implicant is a product term in an SOP expression (or a sum term in POS expression)
    Implicants are always rectangular in shape and the # of 1's covered is a power of 2
  A prime implicant is an implicant that is not fully contained in some other larger implicant
B C A | 00 | 01 | 11 | 10
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1
red  implicant (but not prime) many more are not shown
blue  prime implicants (only two)

## Slide 40
Don’t Care Conditions
  Many times there are incompletely specified conditions
    Valuations that can never occur, or for which we “don’t care what the device does”
  Modeling such a device requires us to specify don’t care conditions in those instances
    Use X as a value to indicate we don't care what happens
  Don't care situations are often called incompletely specified functions

## Slide 41
Example Using Don't Cares
  f(A,B,C,D) = m(1,5,8,9,10) + d(3,7,11,15)
  f = A B' + A' D
C D A B | 00 | 01 | 11 | 10
00 | 0 | 1 | X | 0
01 | 0 | 1 | X | 0
11 | 0 | 0 | X | 0
10 | 1 | 1 | X | 1

## Slide 42
Karnaugh Map Method Restated
  Choose an element from the “on” set
  Find all maximal groups (prime implicants) of “on” elements and X elements adjacent to that element
    Note 1: prime implicants are always a power of 2 in size
    Note 2: do not feel compelled to include X’s – use them only when they provide a larger implicant
  Repeat steps 1-2 for all elements in the “on” set
  Select all essential prime implicants
  For all elements of the “on” set not covered by the essential prime implicants, select the smallest number of prime implicants that cover them

## Slide 43
Example: 7 Segment Display
  Binary Coded Decimal (BCD) input
    4 bit codes: 0000 (0) thru 1001 (9) allowed
    4 bit input code should operate lights of a 7 segment display: codes 1010 – 1111 never occur
    7 output signals – one for each light
a
f b
g
e c
d
WXYZ = 1001 
a
f b
g
c
d
d = 1 is optional

## Slide 44
7 Segment Display Continued
Y Z W X | 00 | 01 | 11 | 10
00 | 1 | 0 | 1 | 1
01 | 0 | 1 | 1 | X
11 | X | X | X | X
10 | 1 | 1 | X | X
W | X | Y | Z | a | b | c | d | e | f | g
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | X | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | X | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | X | 0 | 1 | 1
1 | 0 | 1 | 0 | X | X | X | X | X | X | X
1 | 0 | 1 | 1 | X | X | X | X | X | X | X
1 | 1 | 0 | 0 | X | X | X | X | X | X | X
1 | 1 | 0 | 1 | X | X | X | X | X | X | X
1 | 1 | 1 | 0 | X | X | X | X | X | X | X
1 | 1 | 1 | 1 | X | X | X | X | X | X | X
K-map for a
W + Y + X'Z' + XZ
a =

## Slide 45
Practical 7 Segment Displays
  The lights (LEDs) on a real 7 segment display are always “active low”
    When you want to use our design, just invert all the results
      9  BCD = 1001  abcdefg = 111x011 becomes 000x100
a
f b
g
e c
d